## Slide 1: PNSCR User Manual
NFC MW
v2.0

## Slide 2: Introduction
  PNSCR is the script tool which can be run on target device.
    Supported platform - Android, Linux
    This tool is executable binary runs with root permission under adb shell.
    Working independently with installed NFC MW / eSE-SPI MW
  Support protocol
    - NCI , ISO7816 on SPI
  Purpose
    Can be used in cases below :
      Bring up NFCC/eSE without M/W stack.
      Simulate defect symptom.
      Simulate specific debug mode.
        Dynamic LMA
        Self test
        Read DieID
      Reproduction issues on specific scenario
        Nfcc / eSE concurrent access
        P2P, tag reading

## Slide 3
The package contents
  Libnfc_pnscr source code
    Source nxp_pnscr/libnfcspi-scr/* shall be copied to /vendor/nxp/pnscr/ in Android environment to build.
  Pnscr executable binary
    Shall be pushed to /system/bin folder for execution from Binary folder, binary will support all arm64 target architecture no Android version specific dependency.
  Scripts
    Helper windows batch files for disabling HAL service and exclusive access of NFC/eSE from tool
    Scenario specific PNSCR scripts to be pushed to predefined location /data/nfc
  PNSCR user manual
    About tool Features
    commands supported usage with examples
    Guidelines and limitations
Contents of package

## Slide 4: Executable mode
  3 types of mode
    Types identified by options –t. Supports input parameter 0,1 & 2.
    Type 0 : Line input mode
      Execute by Input NCI CMD in command window
    Type 1 : Script mode
      Execute script
    Type 2 : Hybrid mode
      Script + Line input mode
        Execute script and change to line input mode

## Slide 5: Example of usage
  Example #1.
  Test mode : Script mode
  Script file : “/data/nfc/reset_ntf_reproduction.txt”
  Driver name : “nxp-nci”
    pnscr –t 1 -d nxp-nci –f /data/nfc/reset_ntf_reproduction.txt
  Example #2.
  Test mode : Line input
  Driver name : “nxp-nci”
    pnscr –t 0 –d nxp-nci
here tool will wait for user to enter Command - NCI/HCI commands supported
eg - 20030301A044
  Example #3.
  Test mode : Script + line input
  Script file location : “/data/nfc/issue1.txt”
  Driver name : “nxp-nci”
    pnscr –t 2 -d nxp-nci –f /data/nfc/issue1.txt
    after completing input script execution, tool will wait for user to enter Command - NCI/HCI commands supported.
    eg - 20030301A044

## Slide 6: Command list
  reset
  send
  trigger
  stop
  interval
  sleep
  loop / end
  resetspi
  sendspi
  #,/* */

## Slide 7: Usage of Command
  reset (ven behavior will be various depends on nfcc driver)
    Control mode of NFCC
    reset 0 : turn off NFCC (no impact on ven in case of always on)
    reset 1 : set functional mode
    reset 2 : set download mode
    reset 5 : ven reset (valid only for SN1xx)
  send
    Send data to NFCC
      e.g.) send 21060100 (NCI : RF_DEACTIVATE_CMD)
  trigger
    Wait until receive specified data and resume
    Multiple data can be specified
      e.g.) trigger 6105 : wait until receiving 6105xxxx from CLF
      Once get specific data, then resume the script
      trigger 6105|8115C0 : wait until receiving RF_INTF_ACTIVATED or HCI_ALL_PIPE_CLEARED

## Slide 8: Usage of Command (Cont.)
  stop
    Exit program when it get specified rsp / ntf
    “stop” will not block executing script
    e.g.) stop 6000
    => Program will end if it gets CORE_RESET_NTF
    stop 6105|8115C0 : End program if it receive RF_INTF_ACTIVATED or HCI_ALL_PIPE_CLEARED
  interval
    Default delay between each lines (unit : ms)
    Interval will be updated with new value if it is used in the middle of script

## Slide 9: Usage of Command (Cont.)
  6. sleep
    Wait amount of parameter (unit : ms)
    e.g.) sleep 50 : sleep 50 ms
  7. loop / end
    Start loop as amount of parameter until meet “end”
      e.g.)
      loop 20
      trigger 61070101
      send 2F3304400040D8
      end
      Wait until getting RF on event then send get dynamic LMA response repeat above step 20 times

## Slide 10: Usage of Command (Cont.)
  8. resetspi
    Open/close eSE-spi session
    e.g.) resetspi 1 : open eSE session
    => this will initiate INTF_RESET
      resetspi 0 : close eSE session
      => this will initiate PROP_END_APDU_REQ
  9. sendspi
    send ISO7816-4 apdu to eSE
    e.g.) sendspi 0070000001 : open logical channel
    sendspi 00A4xxxxxxx : select aid xxxx

## Slide 11: Features Supported
Tool is independent of Chip type.
Any driver name can be passed as command argument, however, need to take care of IOCTL command compatibility.
Control VEN/RSTN state of NFCC.
Set NFCC mode normal or download.
Sending NCI & SPI command to NFCC/eSE.
Wait for response/notifications.

## Slide 12: Block Diagram
Get_argv()
  Parsing the input parameters like executable mode, driver & script.
Get_mode()
  Read the script which is passed as runtime argument.
  Decide the ioctl reset value based on reset command mentioned in the script.

## Slide 13: How to execute
Follow the pre-requisite with respect to each script execution.
  Init_deinit, spi test script(pnscr_sn110_init.txt, pnscr_sn110_init_deinit.txt, pnscr_test_spi.txt) -
    Loop count is mentioned in script which can be modified.
  Tag test(pnscr_t2t_test.txt, pnscr_t4t_test.tst) -
    Tag should be placed in proximity before executing script.
    Tag presence check will happen in loop, loop count can be modified in script .
  Host Card Emulation(pnscr_HCE_test.txt) –
    Execute batch script.
    Execute following steps in jcshell
      /term Remote
      /reset
      transitionoverDH 50 200 00 00
    Loop count to jcshell script(first parameter) & in script should be same.
Execute respective batch file.
Note:-
If batch execution is aborted, rename respective HAL file with original library name as mentioned in script to recover HAL service.
In case of switching from Tool mode to MW mode, device shall be rebooted.
Loop count

## Slide 14: SN110 Init Script
Nfc service will not restart after killing because of nfc_nci_nxp_snxxx.so is not present.
After execution, nfc service will be restarted.
Interval – sleep between execution of 2 commands(ms)
Script.txt
Batch file

## Slide 15: Output
Console output of Script mode

## Slide 16
Guidelines
Compatible driver shall be used for IOCTL operations like (VEN RST toggle, DL/Normal Mode etc.)
Script shall be written as per Syntax/Format and prechecked/reviewed.
Total size of command packet buffer length(Header included) limited to 512 bytes due to tool & driver implementation.
Limitations
Only power management IOCTL operations are implemented not all IOCTL operations supported.
The commands execution is script based; tool does not have any response timeout handling.
There is no response validation done at tool side except length check.

## Slide 18: Execution flow for NFC & SPI

## Slide 19: Sequence diagram for NFC & SPI